## What is OSI Model?
The OSI model, created in 1984 by ISO, is a reference framework that explains the process of transmitting data between computers. It is divided into seven layers that work together to carry out specialised network functions, allowing for a more systematic approach to networking.

## What are the 7 layers of the OSI Model?
The OSI model consists of seven abstraction layers arranged in a top-down order:
1. Physical Layer
2. Data Link Layer
3. Network Layer
4. Transport Layer
5. Session Layer
6. Presentation Layer
7. Application Layer
## Physical Layer – Layer 1
The lowest layer of the OSI reference model is the physical layer. It is responsible for the actual physical connection between the devices. The physical layer contains information in the form of bits. It is responsible for transmitting individual bits from one node to the next. When receiving data, this layer will get the signal received and convert it into 0s and 1s and send them to the Data Link layer, which will put the frame back together.

### Functions of the Physical Layer
- Bit synchronization: The physical layer provides the synchronization of the bits by providing a clock. This clock controls both sender and receiver thus providing synchronization at the bit level.
- Bit rate control: The Physical layer also defines the transmission rate i.e. the number of bits sent per second.
- Physical topologies: Physical layer specifies how the different, devices/nodes are arranged in a network i.e. bus, star, or mesh topology.
- Transmission mode: Physical layer also defines how the data flows between the two connected devices. The various transmission modes possible are Simplex, half-duplex and full-duplex.
Note:
1. Hub, Repeater, Modem, and Cables are Physical Layer devices.
2. Network Layer, Data Link Layer, and Physical Layer are also known as Lower Layers or Hardware Layers.
## Data Link Layer (DLL) – Layer 2
The data link layer is responsible for the node-to-node delivery of the message. The main function of this layer is to make sure data transfer is error-free from one node to another, over the physical layer. When a packet arrives in a network, it is the responsibility of the DLL to transmit it to the Host using its MAC address.
The Data Link Layer is divided into two sublayers:
1. Logical Link Control (LLC)
2. Media Access Control (MAC)
The packet received from the Network layer is further divided into frames depending on the frame size of the NIC(Network Interface Card). DLL also encapsulates Sender and Receiver’s MAC address in the header.
The Receiver’s MAC address is obtained by placing an ARP(Address Resolution Protocol) request onto the wire asking “Who has that IP address?” and the destination host will reply with its MAC address.
### Functions of the Data Link Layer
- Framing: Framing is a function of the data link layer. It provides a way for a sender to transmit a set of bits that are meaningful to the receiver. This can be accomplished by attaching special bit patterns to the beginning and end of the frame.
- Physical addressing: After creating frames, the Data link layer adds physical addresses (MAC addresses) of the sender and/or receiver in the header of each frame.
- Error control: The data link layer provides the mechanism of error control in which it detects and retransmits damaged or lost frames.
- Flow Control: The data rate must be constant on both sides else the data may get corrupted thus, flow control coordinates the amount of data that can be sent before receiving an acknowledgment.
- Access control: When a single communication channel is shared by multiple devices, the MAC sub-layer of the data link layer helps to determine which device has control over the channel at a given time.

Note:
1. Packet in the Data Link layer is referred to as Frame.
2. Data Link layer is handled by the NIC (Network Interface Card) and device drivers of host machines.
3. Switch & Bridge are Data Link Layer devices.
## Network Layer – Layer 3
The network layer works for the transmission of data from one host to the other located in different networks. It also takes care of packet routing i.e. selection of the shortest path to transmit the packet, from the number of routes available. The sender & receiver’s IP addresses are placed in the header by the network layer.

### Functions of the Network Layer
- Routing: The network layer protocols determine which route is suitable from source to destination. This function of the network layer is known as routing.
- Logical Addressing: To identify each device on Internetwork uniquely, the network layer defines an addressing scheme. The sender & receiver’s IP addresses are placed in the header by the network layer. Such an address distinguishes each device uniquely and universally.
Note:
1. Segment in the Network layer is referred to as Packet.
2. Network layer is implemented by networking devices such as routers and switches.
## Transport Layer – Layer 4
The transport layer provides services to the application layer and takes services from the network layer. The data in the transport layer is referred to as Segments. It is responsible for the end-to-end delivery of the complete message. The transport layer also provides the acknowledgment of the successful data transmission and re-transmits the data if an error is found.
At the sender’s side: The transport layer receives the formatted data from the upper layers, performs Segmentation, and also implements Flow and error control to ensure proper data transmission. It also adds Source and Destination port numbers in its header and forwards the segmented data to the Network Layer.
Note: The sender needs to know the port number associated with the receiver’s application.
Generally, this destination port number is configured, either by default or manually. For example, when a web application requests a web server, it typically uses port number 80, because this is the default port assigned to web applications. Many applications have default ports assigned.
At the receiver’s side: Transport Layer reads the port number from its header and forwards the Data which it has received to the respective application. It also performs sequencing and reassembling of the segmented data.
### Functions of the Transport Layer
- Segmentation and Reassembly: This layer accepts the message from the (session) layer, and breaks the message into smaller units. Each of the segments produced has a header associated with it. The transport layer at the destination station reassembles the message.
- Service Point Addressing: To deliver the message to the correct process, the transport layer header includes a type of address called service point address or port address. Thus by specifying this address, the transport layer makes sure that the message is delivered to the correct process.
#### Services Provided by Transport Layer
1. Connection-Oriented Service
2. Connectionless Service
1. Connection-Oriented Service: It is a three-phase process that includes
- Connection Establishment
- Data Transfer
- Termination/disconnection
In this type of transmission, the receiving device sends an acknowledgment, back to the source after a packet or group of packets is received. This type of transmission is reliable and secure.
2. Connectionless service: It is a one-phase process and includes Data Transfer. In this type of transmission, the receiver does not acknowledge receipt of a packet. This approach allows for much faster communication between devices. Connection-oriented service is more reliable than connectionless Service.
Note:

1. Data in the Transport Layer is called Segments.
2. Transport layer is operated by the Operating System. It is a part of the OS and communicates with the Application Layer by making system calls.
3. The transport layer is called as Heart of the OSI model.
4. Device or Protocol Use : TCP, UDP  NetBIOS, PPTP
## Session Layer – Layer 5
This layer is responsible for the establishment of connection, maintenance of sessions, and authentication, and also ensures security.
### Functions of the Session Layer
- Session establishment, maintenance, and termination: The layer allows the two processes to establish, use, and terminate a connection.
- Synchronization: This layer allows a process to add checkpoints that are considered synchronization points in the data. These synchronization points help to identify the error so that the data is re-synchronized properly, and ends of the messages are not cut prematurely and data loss is avoided.
- Dialog Controller: The session layer allows two systems to start communication with each other in half-duplex or full-duplex.
Note:
1. All the below 3 layers(including Session Layer) are integrated as a single layer in the TCP/IP model as the ????pplication Layer”.
2. Implementation of these 3 layers is done by the network application itself. These are also known as Upper Layers or Software Layers.
3. Device or Protocol Use :  NetBIOS, PPTP.
For example:-
Let us consider a scenario where a user wants to send a message through some Messenger application running in his browser. The “Messenger” here acts as the application layer which provides the user with an interface to create the data. This message or so-called Data is compressed, encrypted (if any secure data), and converted into bits (0’s and 1’s) so that it can be transmitted.

Communication in Session Layer
## Presentation Layer – Layer 6
The presentation layer is also called the Translation layer. The data from the application layer is extracted here and manipulated as per the required format to transmit over the network.
### Functions of the Presentation Layer
- Translation: For example, ASCII to EBCDIC.
- Encryption/ Decryption: Data encryption translates the data into another form or code. The encrypted data is known as the ciphertext and the decrypted data is known as plain text. A key value is used for encrypting as well as decrypting data.
- Compression: Reduces the number of bits that need to be transmitted on the network.
Note: Device or Protocol Use:  JPEG, MPEG, GIF
## Application Layer – Layer 7
At the very top of the OSI Reference Model stack of layers, we find the Application layer which is implemented by the network applications. These applications produce the data, which has to be transferred over the network. This layer also serves as a window for the application services to access the network and for displaying the received information to the user.
Example: Application – Browsers, Skype Messenger, etc.
Note: 1. The application Layer is also called Desktop Layer.
          2.  Device or Protocol Use :  SMTP

### Functions of the Application Layer
The main functions of the application layer are given below.
- Network Virtual Terminal: It allows a user to log on to a remote host.
- FTAM- File transfer access and management: This application allows a user to
  access files in a remote host, retrieve files in a remote host, and manage or
  control files from a remote computer.
- Mail Services: Provide email service.
- Directory Services: This application provides distributed database sources
  and access for global information about various objects and services.
Note: OSI model acts as a reference model and is not implemented on the Internet because of its late invention. The current model being used is the TCP/IP model.
## What is the Flow of Data in OSI Model?
When we transfer information from one device to another, it travels through 7 layers of OSI model. First data travels down through 7 layers from the sender’s end and then climbs back 7 layers on the receiver’s end.
Let’s look at it with an Example:
Luffy sends an e-mail to his friend Zoro.
Step 1: Luffy interacts with e-mail application like Gmail, outlook, etc. Writes his email to send. (This happens in Layer 7: Application layer)
Step 2: Mail application prepares for data transmission like encrypting data and formatting it for transmission. (This happens in Layer 6: Presentation Layer)
Step 3: There is a connection established between the sender and receiver on the internet. (This happens in Layer 5: Session Layer)
Step 4: Email data is broken into smaller segments. It adds sequence number and error-checking information to maintain the reliability of the information. (This happens in Layer 4: Transport Layer)
Step 5: Addressing of packets is done in order to find the best route for transfer. (This happens in Layer 3: Network Layer)

Step 6: Data packets are encapsulated into frames, then MAC address is added for local devices and then it checks for error using error detection. (This happens in Layer 2: Data Link Layer)
Step 7: Lastly Frames are transmitted in the form of electrical/ optical signals over a physical network medium like ethernet cable or WiFi.
After the email reaches the receiver i.e. Zoro, the process will reverse and decrypt the e-mail content. At last, the email will be shown on Zoro’s email client.
## Advantages of OSI Model
OSI Model defines the communication of a computing system into 7 different layers. Advantages of OSI Model include:
- It divides network communication into 7 layers which makes it easier to understand and troubleshoot.
- It standardizes network communications, as each layer has fixed functions and protocols.
- Diagnosing network problems is easier with the OSI model.
- It is easier to improve with advancements as each layer can get updates separately.
## OSI Model in a Nutshell
Layer No	Layer Name	Responsibility	Information Form(Data Unit)	Device or Protocol
7	Application Layer	Helps in identifying the client and synchronizing communication.	Message	SMTP
6	Presentation Layer	Data from the application layer is extracted and manipulated in the required format for transmission.	Message	JPEG, MPEG, GIF
5	Session Layer	Establishes Connection, Maintenance, Ensures Authentication and Ensures security.	Message	Gateway
4	Transport Layer	Take Service from Network Layer and provide it to the Application Layer.	Segment	Firewall
3	Network Layer	Transmission of data from one host to another, located in different networks.	Packet	Router
2	Data Link Layer	Node to Node Delivery of Message.	Frame	Switch, Bridge
1	Physical Layer	Establishing Physical Connections between Devices.	Bits	Hub, Repeater, Modem, Cables

## OSI vs TCP/IP Model
Some key differences between the OSI model and the TCP/IP Model are:
1. TCP/IP model consists of 4 layers but OSI model has 7 layers. Layers 5,6,7 of the OSI model are combined into the Application Layer of TCP/IP model and OSI layers 1 and 2 are combined into Network Access Layers of TCP/IP protocol.
2. The TCP/IP model is older than the OSI model, hence it is a foundational protocol that defines how should data be transferred online.
3. Compared to the OSI model, the TCP/IP model has less strict layer boundaries.
4. All layers of the TCP/IP model are needed for data transmission but in the OSI model, some applications can skip certain layers. Only layers 1,2 and 3 of the OSI model are necessary for data transmission.
Did you Know?
TCP/IP protocol ( Transfer Control Protocol/Internet Protocol ) was created by U.S. Department of Defense’s Advanced Research Projects Agency (ARPA) in 1970s.
We have discussed about What is OSI model?, What are layers of OSI model, How data flows in the 7 layers of OSI model, and the differences between TCP/IP protocol and OSI protocol.
## OSI Model – FAQs
### Is OSI layer still used?
Yes, the OSI model is still used by networking professionals to understand data abstraction paths and processes better.
### What is the highest layer of the OSI model?
Layer 7 or Application layer is highest layer of OSI model.

## What Does TCP/IP Do?
The main work of TCP/IP is to transfer the data of a computer from one device to another. The main condition of this process is to make data reliable and accurate so that the receiver will receive the same information which is sent by the sender. To ensure that, each message reaches its final destination accurately, the TCP/IP model divides its data into packets and combines them at the other end, which helps in maintaining the accuracy of the data while transferring from one end to another end.
## What is the Difference between TCP and IP?
TCP and IP are different protocols of Computer Networks. The basic difference between TCP (Transmission Control Protocol) and IP (Internet Protocol) is in the transmission of data. In simple words, IP finds the destination of the mail and TCP has the work to send and receive the mail. UDP is another protocol, which does not require IP to communicate with another computer. IP is required by only TCP. This is the basic difference between TCP and IP.
## How Does the TCP/IP Model Work?
Whenever we want to send something over the internet using the TCP/IP Model, the TCP/IP Model divides the data into packets at the sender’s end and the same packets have to be recombined at the receiver’s end to form the same data, and this thing happens to maintain the accuracy of the data. TCP/IP model divides the data into a 4-layer procedure, where the data first go into this layer in one order and again in reverse order to get organized in the same way at the receiver’s end.

For more, you can refer to TCP/IP in Computer Networking.
## Layers of TCP/IP Model
1. Application Layer
2. Transport Layer(TCP/UDP)
3. Network/Internet Layer(IP)
4. Data Link Layer (MAC)
5. Physical Layer
The diagrammatic comparison of the TCP/IP and OSI model is as follows:

TCP/IP and OSI
### 1. Physical Layer
It is a group of applications requiring network communications. This layer is responsible for generating the data and requesting connections. It acts on behalf of the sender and the Network Access layer on the behalf of the receiver. During this article, we will be talking on the behalf of the receiver.
### 2. Data Link Layer
The packet’s network protocol type, in this case, TCP/IP, is identified by the data-link layer. Error prevention and “framing” are also provided by the data-link layer. Point-to-Point Protocol (PPP) framing and Ethernet IEEE 802.2 framing are two examples of data-link layer protocols.
### 3. Internet Layer
This layer parallels the functions of OSI’s Network layer. It defines the protocols which are responsible for the logical transmission of data over the entire network. The main protocols residing at this layer are as follows:
- IP: IP stands for Internet Protocol and it is responsible for delivering packets from the source host to the destination host by looking at the IP addresses in the packet headers. IP has 2 versions: IPv4 and IPv6. IPv4 is the one that most websites are using currently. But IPv6 is growing as the number of IPv4 addresses is limited in number when compared to the number of users.
- ICMP: ICMP stands for Internet Control Message Protocol. It is encapsulated within IP datagrams and is responsible for providing hosts with information about network problems.
- ARP: ARP stands for Address Resolution Protocol. Its job is to find the hardware address of a host from a known IP address. ARP has several types: Reverse ARP, Proxy ARP, Gratuitous ARP, and Inverse ARP.
The Internet Layer is a layer in the Internet Protocol (IP) suite, which is the set of protocols that define the Internet. The Internet Layer is responsible for routing packets of data from one device to another across a network. It does this by assigning each device a unique IP address, which is used to identify the device and determine the route that packets should take to reach it.

Example: Imagine that you are using a computer to send an email to a friend. When you click “send,” the email is broken down into smaller packets of data, which are then sent to the Internet Layer for routing. The Internet Layer assigns an IP address to each packet and uses routing tables to determine the best route for the packet to take to reach its destination. The packet is then forwarded to the next hop on its route until it reaches its destination. When all of the packets have been delivered, your friend’s computer can reassemble them into the original email message.
In this example, the Internet Layer plays a crucial role in delivering the email from your computer to your friend’s computer. It uses IP addresses and routing tables to determine the best route for the packets to take, and it ensures that the packets are delivered to the correct destination. Without the Internet Layer, it would not be possible to send data across the Internet.
### 4. Transport Layer
The TCP/IP transport layer protocols exchange data receipt acknowledgments and retransmit missing packets to ensure that packets arrive in order and without error. End-to-end communication is referred to as such. Transmission Control Protocol (TCP) and User Datagram Protocol are transport layer protocols at this level (UDP).
- TCP: Applications can interact with one another using TCP as though they were physically connected by a circuit. TCP transmits data in a way that resembles character-by-character transmission rather than separate packets. A starting point that establishes the connection, the whole transmission in byte order, and an ending point that closes the connection make up this transmission.
- UDP: The datagram delivery service is provided by UDP, the other transport layer protocol. Connections between receiving and sending hosts are not verified by UDP. Applications that transport little amounts of data use UDP rather than TCP because it eliminates the processes of establishing and validating connections.
### 5. Application Layer
This layer is analogous to the transport layer of the OSI model. It is responsible for end-to-end communication and error-free delivery of data. It shields the upper-layer applications from the complexities of data. The three main protocols present in this layer are:
- HTTP and HTTPS: HTTP stands for Hypertext transfer protocol. It is used by the World Wide Web to manage communications between web browsers and servers. HTTPS stands for HTTP-Secure. It is a combination of HTTP with SSL(Secure Socket Layer). It is efficient in cases where the browser needs to fill out forms, sign in, authenticate, and carry out bank transactions.
- SSH: SSH stands for Secure Shell. It is a terminal emulations software similar to Telnet. The reason SSH is preferred is because of its ability to maintain the encrypted connection. It sets up a secure session over a TCP/IP connection.
- NTP: NTP stands for Network Time Protocol. It is used to synchronize the clocks on our computer to one standard time source. It is very useful in situations like bank transactions. Assume the following situation without the presence of NTP. Suppose you carry out a transaction, where your computer reads the time at 2:30 PM while the server records it at 2:28 PM. The server can crash very badly if it’s out of sync.
The host-to-host layer is a layer in the OSI (Open Systems Interconnection) model that is responsible for providing communication between hosts (computers or other devices) on a network. It is also known as the transport layer.
Some common use cases for the host-to-host layer include:
1. Reliable Data Transfer: The host-to-host layer ensures that data is transferred reliably between hosts by using techniques like error correction and flow control. For example, if a packet of data is lost during transmission, the host-to-host layer can request that the packet be retransmitted to ensure that all data is received correctly.
2. Segmentation and Reassembly: The host-to-host layer is responsible for breaking up large blocks of data into smaller segments that can be transmitted over the network, and then reassembling the data at the destination. This allows data to be transmitted more efficiently and helps to avoid overloading the network.
3. Multiplexing and Demultiplexing: The host-to-host layer is responsible for multiplexing data from multiple sources onto a single network connection, and then demultiplexing the data at the destination. This allows multiple devices to share the same network connection and helps to improve the utilization of the network.
4. End-to-End Communication: The host-to-host layer provides a connection-oriented service that allows hosts to communicate with each other end-to-end, without the need for intermediate devices to be involved in the communication.
Example: Consider a network with two hosts, A and B. Host A wants to send a file to host B. The host-to-host layer in host A will break the file into smaller segments, add error correction and flow control information, and then transmit the segments over the network to host B. The host-to-host layer in host B will receive the segments, check for errors, and reassemble the file. Once the file has been transferred successfully, the host-to-host layer in host B will acknowledge receipt of the file to host A.
In this example, the host-to-host layer is responsible for providing a reliable connection between host A and host B, breaking the file into smaller segments, and reassembling the segments at the destination. It is also responsible for multiplexing and demultiplexing the data and providing end-to-end communication between the two hosts.
## Other Common Internet Protocols
TCP/IP Model covers many Internet Protocols. The main rule of these Internet Protocols is how the data is validated and sent over the Internet. Some Common Internet Protocols include:
- HTTP (Hypertext Transfer Protocol): HTTP takes care of Web Browsers and Websites.
- FTP (File Transfer Protocol): FTP takes care of how the file is to be sent over the Internet.
- SMTP (Simple Mail Transfer Protocol): SMTP is used to send and receive data.
## Difference between TCP/IP and OSI Model
TCP/IP	OSI
TCP refers to Transmission Control Protocol.	OSI refers to Open Systems Interconnection.
TCP/IP uses both the session and presentation layer in the application layer itself.	OSI uses different session and presentation layers.
TCP/IP follows connectionless a horizontal approach.	OSI follows a vertical approach.
The Transport layer in TCP/IP does not provide assurance delivery of packets.	In the OSI model, the transport layer provides assurance delivery of packets.
Protocols cannot be replaced easily in TCP/IP model.	While in the OSI model, Protocols are better covered and are easy to replace with the technology change.
TCP/IP model network layer only provides connectionless (IP) services. The transport layer (TCP) provides connections.	Connectionless and connection-oriented services are provided by the network layer in the OSI model.

## FAQ:
### Q.1 Which IP Addresses Do TCP/IP Work With?
Answer:
TCP/IP generally works with both the IP that is, IPv4 and IPv6. If you are using IPv4 or IPv6, it seems that you are already working on TCP/IP Model.

# Computer Network | Leaky bucket algorithm
In the network layer, before the network can make Quality of service guarantees, it must know what traffic is being guaranteed. One of the main causes of congestion is that traffic is often bursty.
To understand this concept first we have to know little about traffic shaping. Traffic Shaping is a mechanism to control the amount and the rate of traffic sent to the network. Approach of congestion management is called Traffic shaping. Traffic shaping helps to regulate the rate of data transmission and reduces congestion.

There are 2 types of traffic shaping algorithms:
1. Leaky Bucket
2. Token Bucket
Suppose we have a bucket in which we are pouring water, at random points in time, but we have to get water at a fixed rate, to achieve this we will make a hole at the bottom of the bucket. This will ensure that the water coming out is at some fixed rate, and also if the bucket gets full, then we will stop pouring water into it.

The input rate can vary, but the output rate remains constant. Similarly, in networking, a technique called leaky bucket can smooth out bursty traffic. Bursty chunks are stored in the bucket and sent out at an average rate.

In the above figure, we assume that the network has committed a bandwidth of 3 Mbps for a host. The use of the leaky bucket shapes the input traffic to make it conform to this commitment. In the above figure, the host sends a burst of data at a rate of 12 Mbps for 2s, for a total of 24 Mbits of data. The host is silent for 5 s and then sends data at a rate of 2 Mbps for 3 s, for a total of 6 Mbits of data. In all, the host has sent 30 Mbits of data in 10 s. The leaky bucket smooths out the traffic by sending out data at a rate of 3 Mbps during the same 10 s.

Without the leaky bucket, the beginning burst may have hurt the network by consuming more bandwidth than is set aside for this host. We can also see that the leaky bucket may prevent congestion.
A simple leaky bucket algorithm can be implemented using FIFO queue. A FIFO queue holds the packets. If the traffic consists of fixed-size packets (e.g., cells in ATM networks), the process removes a fixed number of packets from the queue at each tick of the clock. If the traffic consists of variable-length packets, the fixed output rate must be based on the number of bytes or bits.
The following is an algorithm for variable-length packets:
1. Initialize a counter to n at the tick of the clock.
2. Repeat until n is smaller than the packet size of the packet at the head of the queue.
  1. Pop a packet out of the head of the queue, say P.
  2. Send the packet P, into the network
  3. Decrement the counter by the size of packet P.
3. Reset the counter and go to step 1.
Note: In the below examples, the head of the queue is the rightmost position and the tail of the queue is the leftmost position.
Example: Let n=1000
Packet=

Since n > size of the packet at the head of the Queue, i.e. n > 200
Therefore, n = 1000-200 = 800
Packet size of 200 is sent into the network.

Now, again n > size of the packet at the head of the Queue, i.e. n > 400
Therefore, n = 800-400 = 400
Packet size of 400 is sent into the network.

Since, n < size of the packet at the head of the Queue, i.e.  n < 450
Therefore, the procedure is stopped.
Initialise n = 1000 on another tick of the clock.
This procedure is repeated until all the packets are sent into the network.
Below is the implementation of above explained approach:

// cpp program to implement leakybucket / #include <bits/stdc++.h> / using namespace std; / int main() / { / int no_of_queries, storage, output_pkt_size; / int input_pkt_size, bucket_size, size_left; / // initial packets in the bucket / storage = 0; / // total no. of times bucket content is checked / no_of_queries = 4; / // total no. of packets that can / // be accommodated in the bucket / bucket_size = 10; / // no. of packets that enters the bucket at a time / input_pkt_size = 4; / // no. of packets that exits the bucket at a time / output_pkt_size = 1; / for (int i = 0; i < no_of_queries; i++) // space left / { / size_left = bucket_size - storage; / if (input_pkt_size <= size_left) { / // update storage / storage += input_pkt_size; / } / else { / printf("Packet loss = %d\n", input_pkt_size); / } / printf("Buffer size= %d out of bucket size= %d\n", / storage, bucket_size); / storage -= output_pkt_size; / } / return 0; / } / // This code is contributed by bunny09262002 / // Improved by: rishitchaudhary

Output

Buffer size= 4 out of bucket size= 10
Buffer size= 7 out of bucket size= 10
Buffer size= 10 out of bucket size= 10
Packet loss = 4
Buffer size= 9 out of bucket size= 10
Difference between Leaky and Token buckets –

Leaky Bucket	Token Bucket
When the host has to send a packet , packet is thrown in bucket.	In this, the bucket holds tokens generated at regular intervals of time.
Bucket leaks at constant rate	Bucket has maximum capacity.
Bursty traffic is converted into uniform traffic by leaky bucket.	If there is a ready packet , a token is removed from Bucket and packet is send.
In practice bucket is a finite queue outputs at finite rate	If there is no token in the bucket, then the packet cannot be sent.

Some advantage of token Bucket over leaky bucket
- If a bucket is full in tokens Bucket, tokens are discard not packets. While in leaky bucket, packets are discarded.
- Token Bucket can send large bursts at a faster rate while leaky bucket always sends packets at constant rate.
- Predictable Traffic Shaping: Token Bucket offers more predictable traffic shaping compared to leaky bucket. With token bucket, the network administrator can set the rate at which tokens are added to the bucket, and the maximum number of tokens that the bucket can hold. This allows for better control over the network traffic and can help prevent congestion.
- Better Quality of Service (QoS): Token Bucket provides better QoS compared to leaky bucket. This is because token bucket can prioritize certain types of traffic by assigning different token arrival rates to different classes of packets. This ensures that important packets are sent first, while less important packets are sent later, helping to ensure that the network runs smoothly.
- More efficient use of network bandwidth: Token Bucket allows for more efficient use of network bandwidth as it allows for larger bursts of data to be sent at once. This can be useful for applications that require high-speed data transfer or for streaming video content.
- More granular control: Token Bucket provides more granular control over network traffic compared to leaky bucket. This is because it allows the network administrator to set the token arrival rate and the maximum token count, which can be adjusted according to the specific needs of the network.
- Easier to implement: Token Bucket is generally considered easier to implement compared to leaky bucket. This is because token bucket only requires the addition and removal of tokens from a bucket, while leaky bucket requires the use of timers and counters to determine when to release packets.
Some Disadvantage of token Bucket over leaky bucket
- Tokens may be wasted: In Token Bucket, tokens are generated at a fixed rate, even if there is no traffic on the network. This means that if no packets are sent, tokens will accumulate in the bucket, which could result in wasted resources. In contrast, with leaky bucket, the network only generates packets when there is traffic, which helps to conserve resources.
- Delay in packet delivery: Token Bucket may introduce delay in packet delivery due to the accumulation of tokens. If the token bucket is empty, packets may need to wait for the arrival of new tokens, which can lead to increased latency and packet loss.
- Lack of flexibility: Token Bucket is less flexible compared to leaky bucket in terms of shaping network traffic. This is because the token generation rate is fixed, and cannot be changed easily to meet the changing needs of the network. In contrast, leaky bucket can be adjusted more easily to adapt to changes in network traffic.
- Complexity: Token Bucket can be more complex to implement compared to leaky bucket, especially when different token generation rates are used for different types of traffic. This can make it more difficult for network administrators to configure and manage the network.
- Inefficient use of bandwidth: In some cases, Token Bucket may lead to inefficient use of bandwidth. This is because Token Bucket allows for large bursts of data to be sent at once, which can cause congestion and lead to packet loss. In contrast, leaky bucket helps to prevent congestion by limiting the amount of data that can be sent at any given time.